## Slide 1
Sponge Quake Shear Box
- Stick-slip behavior of unstable patch in stable zone -
Geosc 597-3 Class project - 2016F
Kyungjae Im

## Slide 2
Problem Description
Natural earthquakes are in 3-D
- Critical nucleation length Lc ~ G·Dc/[(b-a)σ]
- Frictional properties are complexly distributed
Coseismic and postseismic slip of 2004 parkfield earthquake [Johanson et. al. 2006]
Simulation of repeating earthquakes with different
nucleation patch size [Chen et. al. 2010]

## Slide 3
Problem Description
Why laboratory 1+ dimensional slip are difficult?  Rock is too stiff
Large apparatus dimension required
Deformation is tiny
Lc ~ G·Dc/[(b-a)σ]
(G ~10GPa)
Fault nucleation experiment and simulation with 30cm PMMA
[Latour et. al. 2013, Kaneko et. al 2016]
Rupture propagation experiment with 2m granite
[McLaskey et. al. 2015]

## Slide 4
Solution
Soft & Elastic Material

## Slide 5
Solution
Solution Requirements
Soft & elastic material
Uniform normal & shear stress distribution
Unstable patch within stable surface
Deformation measurement
Soft & Elastic Material
Unsatble patch (a-b)<0
Satble surface (a-b)>0
Satble surface (a-b)>0
Normal force
Shear force
Normal and shear stress distribution
with given configuration
deformation measurement

## Slide 6
Solution
Mechanical Framework
Some sketches

## Slide 7
Solution
Final Mechanical Design
Linear Actuator
Slip surface
Alluminum U-channel frame
Guide Rail
Carrige and
slider (3D printed)
Normal stress adjusted with
Inserting thickness pre-measured papers

## Slide 8
Solution
Measurement
Initial Idea: Flex sensor
But resolution were poor….
Revised Idea: DCDT
pin

## Slide 9
Solution
Electric circuit diagram
Arduino
Linear
Actuator
(Actuonix L12)
5V
GND
+
-
DCDT
(TRANS-TEK 244)
DC Power
A0
Output
30V
GND
+
-
GND
Forward operation
Backward operation

## Slide 10
Demonstration

## Slide 11
Experimental Setup
Rubber patch size (cm): 0.5, 1.0, 1.5, 2.0, 2.5, 3.0, 3.5, 4.0, 4.5, 5.0, 5.5, 6.0
12 patch size with 8 Normal stress were tested
Paper count | 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70
Normal Force (N) | 1.6 | 4.3 | 7.1 | 9.8 | 12.5 | 15.3 | 18.0 | 20.8
Noarmal Stress (kPa) | 0.5 | 1.3 | 2.2 | 3.0 | 3.9 | 4.7 | 5.6 | 6.4
[1 paper (0.7mm): 2.74 N, Surface Area: 0.12 × 0.27 m2]
Normal Force

## Slide 12
Result
Stable sliding vs. stick slip
2.5cm / 4.3 N
5.0cm / 12.5 N

## Slide 13
Result
Maximum velocities
Velocity
(m/s)

## Slide 14
Result
(Apparent) Stability and Discussion
Stable + unstable
Unstable stick-slip
Stable sliding
Velocity
(m/s)
Seem to be solely dependent on patch size?
Why not this? (Lc ~ 1/σ)

## Slide 15
Problems and Further Upgrade Items
Resolution and sampling interval
- Resolution: ~5μm (Arduino 10 bit 1023 interval with 5.5mm)
- Sampling interval: ~20ms
Results vari with sponge and surface condition (Sponge stiffness decreases with deformation experience)
Longer sponge is required to provide better normal and shear stress condition
Multiple loading velocity is required
Gouge?

## Slide 16
Thank You